## Slide 1: Natural Language Processing

## Slide 2: Language Processor

## Slide 3: Speech Recognition Disciplines
Signal Processing: Spectral analysis.
Physics (Acoustics): Study of Sound
Pattern Recognition: Data Clustering
Information Theory: Statistical Models
Linguistics: Grammar and Language Structures
  Morphology: Language structure
  Phonology: Classification of linguistic sounds
  Semantics: Study of meaning
  Pragmatics: How language is used
Physiology: Human Speech Production and Perception
Computer Science: Devise Efficient Algorithms
Note: Understanding of human speech recognition is rudimentary

## Slide 4: Natural Language Applications
Phone and tablet applications
Dictation
Real time vocal tract visualization
Speaker identification and/or verification
Language translation
Robot interaction
Expert systems
Audio databases
Personal assistant
Audio device command and control

## Slide 5: Application Requirements
Long-term benefit after the novelty wears off
Intuitive and easy to use
Easy recovery in presence of mistakes
  Self-correction algorithms when possible
  Verification before proceeding
  Automatic transfer to human operator
  Backup mode of communication (spell the command)
Accuracy of 95% or better in less than optimal environments
Real time response (250 MS or less)

## Slide 6: Technical Issues
Language dependent or independent
  Grammatical models (context, semantics, idioms)
  Number of languages supported
  Assessing meaning to words not in the dictionary
  Available language-based resources
Consistently achieving 95% accuracy or better
  Speech enhancement algorithms
  Filtering background noise and transmission distortions
  Voice activity detection
  Detect boundaries between speech segments
  Handling the slurring of words and co-articulation
Training requirements

## Slide 7: Implementation Classifications

## Slide 8: Speech Recognition
SpEECH
Why Hard?
  A time-varying signal
  Well-structured process
  Limited, known physical movements
  40-60 distinct units (phonemes) per language
  Enhanced to overcome noise
 should be easy!??
  Speaker variations; accents
  Changes in speed, loudness, and pitch
  Environmental noise
  Slurred, bad grammar
  Fuzzy phoneme boundaries
  Context-based semantics
  Large vocabulary
  Signal redundancies

## Slide 9: The Noisy Channel
What is this English sentence? “ay d ih s h er d s ah m th in ng ah b aw ya m uh v ih ng r ih s en l ih”
Where are the word boundaries?
The speech is slurred with grammar errors
Recognition is possible because:
  We are sure of the phonetic components
  We know the language (English)
As easy on the mouth as possible to still be understood

## Slide 10: Robot-human dialog
Robo: “Hi, my name is Robo. I am looking for work to raise funds for Natural Language Processing research.”
Person: “Do you know how to paint?”
Robo: “I have successfully completed training in this skill.”
Person: “Great! The porch needs painting. Here are the brushes and paint.”
Robot rolls away efficiently. An hour later he returns.
Robo: “The task is complete.”
Person: “That was fast, here is your salary; good job, and come back again.”
Robo speaks while rolling away with the payment.
Robo: “The car was not a Porche; it was a Mercedes.”
99% accuracy

## Slide 11: Semantic Issues Sentence: “I made her duck”
  I cooked waterfowl for her.
  I stole her waterfowl and cooked it.
  I created a living waterfowl for her.
  I caused her to bid low in the game of bridge.
  I created the plastic duck that she owns.
  I caused her to quickly lower her head or body.
  I waved my magic wand and turned her into waterfowl.
  I caused her to avoid the test.
Eight possible meanings

## Slide 12: How would a computer do?
  I cdnuolt blveiee that I cluod aulaclty uesdnatnrd what I was rdgnieg.
  The phaonmneal pweor of the hmuan mnid Aoccdrnig to rscheearch at Cmabridgde Uinervtisy, it deosn't mttaer in what oredr the ltteers in a word are, the olny iprmoatnt tihng is that the frist and lsat ltteer be in the rghit pclae.
  The rset can be a taotl mses and you can still raed it wouthit a problem.
  This is bcuseae the huamn mnid deos not raed ervey lteter by istlef, but the word as a wlohe.
  Amzanig huh?
  Yaeh and I awlyas thought slpeling was ipmorantt!

## Slide 13: Language Components
Phoneme: Smallest discrete unit of sound that distinguishes words (Minimal Pair Principle)
Syllable: Acoustic component perceived as a single unit
Morpheme: Smallest linguistic unit with meaning
Word: Speaker identifiable unit of meaning
Phrase: Sub-message of one or more words
Sentence: Self-contained message derived from a sequence of phrases and words

## Slide 14: Natural Language Characteristics
Phones: Set of all possible sounds that humans can articulate.
Each language selects a set of phonemes from the larger set of phones (English ≈ 40). Our hearing is tuned to respond to this smaller set.
Speech is a highly redundant sequential signal containing a sequence of sounds (phonemes) , pitch (prosody), gestures, and other expressions that vary with time.

## Slide 15: The Speech Signal
A complex wave of varying atmospheric pressure traveling through space
The pressure is measured (sampled) at regular intervals to produce a digital array of amplitudes
Speech frequencies of interest are 100 to 3400 samples per second
The Nyquist theorem requires measurements of at least double the frequencies of interest

## Slide 16: Nyquist Theorem
Sampling at 1.5 times per cycle
The sample rate must be at least twice the rate of the highest frequency of interest

## Slide 17: Speech Signal Redundancy
Original Continuous Analog Signal
  Virtually contains an infinite number of frequencies
Sampling Rates (Measurements per second)
  Mac: 44,100 2-byte samples per second (705kbps)
  PC: 16,000 2-byte samples per second (256kbps)
  Telephone: 8k 1-byte sample per second (64kbps)
Compression for communication
  Code Excited Linear Prediction Compression: 8kbps
  Research: 4kbps, 2.4 kbps
  Military applications: 600 bps
  Human brain: 50 bps

## Slide 18: Speech Recognition
Goal: Automatically extract the string of words spoken from the speech signal
Speech
Recognition
Words
“How are you?”
Speech Signal

## Slide 19: Speech Physiology
Acoustic Speech Signal
Perception
Production

## Slide 20: Sound Transmission
Top: “this is a demo” Bottom: “A goat …. A coat”
ACORNS Sound Editor is Downloadable (ACORNS web-site)
Time Domain: 8k – 44.1k Samples per second

## Slide 21: Time vs. Frequency Domain
Time Domain: Signal is a composite wave of different frequencies
Frequency Domain: Split time domain into the individual frequencies
Fourier: We can compute the phase and amplitude of each composite sinusoid
FFT: An efficient algorithm to perform the decomposition

## Slide 22: Complex Wave Patterns
Sine waves combine to form a new wave of a different shape
Every complex wave pattern consists of a series of composite sine waves
All of the composite sine are multiples of a basic frequency
Speech mostly consists of sinusoids combined together by linear addition

## Slide 23: Frequency Domain
Narrow band: Shows harmonics – horizontal lines
Harmonic definition: Integral multiple of a basic frequency
Wide Band: Shows pitch – pitch periods are vertical lines
Audio: “This is a Demo”
Horizontal = time, vertical = frequency, frequency amplitude = darkness

## Slide 24: Speech Recognition
Speech
Recognition
Words
“How are you?”
Acoustic Speech Signal
Language Model
Input
Speech
Acoustic
Front-end
Acoustic Models
P(A|W)
Recognized
Utterance
Search
Language Model
P(W)
Processing

## Slide 25: Vocal Tract (for Speech Production)
Note: Velum (soft palate) position controls nasal sounds, epiglottis closes when swallowing
Notes: Labia: lips
Dental: teeth
Alveolar ridge: Area of angle change behind the teeth
Hard palate: The hard roof of the mouth
Soft palate: Soft area behind the hard palate
Uvula: Dangling fleshy soft tissue at the back of the soft palate
Pharynx: cavity between roof of tongue and walls of the upper throat
Tongue blade: flat surface of the tongue behind the tip
Tong body/dorsum: Main portion of tongue below the palates
Tongue root: portion of the tongue in the throat
Epiglottis: Fold of tissue just below the tongue root, covers the larynx when swallowing
Glottis: Opening between the vocal cords.
Larynx: The structure that manipulates the vocal cords

## Slide 26: Another look at the vocal tract

## Slide 27: Vocal Source
Speaker alters vocal tension of the vocal folds
  Opened folds, speech is unvoiced resembling noise
  If folds are stretched close, speech is voiced
Air pressure builds and vocal folds blow open releasing pressure and elasticity causes the vocal folds to fall back
Average fundamental frequency (F0): 60 Hz to 300 Hz
Speakers control vocal tension to alter F0 and the perceived pitch
Closed
Open
Period

## Slide 28: Different Voices
Falsetto – The vocal cords are stretched and become thin causing high frequency
Creaky – Only the front vocal folds vibrate, giving a low frequency
Breathy – Vocal cords vibrate, but air is escaping through the glottis
Each person tends to consistently use particular phonation patterns. This makes the voice uniquely theirs

## Slide 29: Place of the Articulation
Bilabial – The two lips (p, b, and m)
Labio-dental – Lower lip and the upper teeth (v)
Dental – Upper teeth and tongue tip or blade (thing)
Alveolar –Alveolar ridge + tongue tip or blade (d, n, s)
Post alveolar –Area just behind the alveolar ridge and tongue tip or blade (jug ʤ, ship ʃ, chip ʧ, vision ʒ)
Retroflex – Tongue curled and back (rolling r)
Palatal – Tongue body touches the hard palate (j)
Velar – Tongue body touches soft palate (k, g, ŋ (thing))
Glottal – larynx (uh-uh, voiced h)
Articulation: Shaping the speech sounds

## Slide 30: Manner of Articulation
Voiced: The vocal cords are vibrating, Unvoiced: vocal cords don’t vibrate
Obstruent: Frequency domain is similar to noise
  Fricative: Air flow not completely shut off
  Affricate: A sequence of a stop followed by a fricative
  Sibilant: a consonant characterized by a hissing sound (like s or sh)
Trill: A rapid vibration of one speech organ against another (Spanish r).
Aspiration: burst of air following a stop.
Stop: Air flow is cut off
  Ejective: airstream and the glottis are closed and suddenly released (/p/).
  Plosive: Voiced stop followed by sudden release
  Flap: A single, quick touch of the tongue (t in water).
Nasality: Lowering the soft palate allows air to flow through the nose
Glides: vowel-like, syllable position makes them short without stress (w, y). An On-glide is a glide before a vowel; an off-glide is a glide after vowel
Approximant (semi-vowels): Active articulator approaches the passive articulator, but doesn’t totally shut of (L and R).
Lateral: The air flow proceeds around the side of the tongue

## Slide 31: Vowels
Diphthong: Syllabics which show a marked glide from one vowel to another, usually a steady vowel plus a glide
Nasalized: Some air flow through the nasal cavity
Rounding: Shape of the lips
Tense: Sound more extreme (further from the schwa) and tend to have the tongue body higher
Relaxed: Sounds closer to schwa (tonally neutral)
Tongue position: Front to back, high to low
No restriction of the vocal tract, articulators alter the formants
Schwa: unstressed central vowel (“ah”)

## Slide 32: Consonants
Significant obstruction in the nasal or oral cavities
Occur in pairs or triplets and can be voiced or unvoiced
Sonorant: continuous voicing
Unvoiced: less energy
Plosive: Period of silence and then sudden energy burst
Lateral, semi vowels, retroflex: partial air flow block
Fricatives, affricatives: Turbulence in the wave form

## Slide 33: English Consonants
Type | Phones | Mechanism
Plosive | b,p,d,t,g,k | Close oral cavity
Nasal | m, n, ng | Open nasal cavity
Fricative | v,f,z,s,dh,th,zh, sh | Turbulent
Affricate | jh, ch | Stop + Turbulent
Retroflex Liquid | r | Tongue high and curled
Lateral liquid | l | Side airstreams
Glide | w, y | Vowel like

## Slide 34: Consonant Place and Manner
 | Labial | Labio-dental | Dental | Aveolar | Palatal | Velar | Glottal
Plosive | p b |  |  | t d |  | k g | ?
Nasal | m |  |  | n |  | ng | 
Fricative |  | f v | th dh | s z | sh zh |  | h
Retroflex sonorant |  |  |  | r |  |  | 
Lateral sonorant |  |  |  | l |  |  | 
Glide | w |  |  |  | y |  | 

## Slide 35: Example word

## Slide 36: Speech Production Analysis
Devices used to measure speech production
Plate attached to roof of mouth measuring contact
Collar around the neck measuring glottis vibrations
Measure air flow from mouth and nose
Three dimension images using MRI
Note: The International Phonetic Alphabet (IPA) was designed before the above technologies existed. They were devised by a linguist looking down someone’s mouth or feeling how sounds are made.

## Slide 37: ARPABET: English-based phonetic system
Phone Example Phone Example Phone Example
[iy] beat [b] bet [p] pet
[ih] bit [ch] chet [r] rat
[eh] bet [d] debt [s] set
[ah] but [f] fat [sh] shoe
[x] bat [g] get [t] ten
[ao] bought [hh] hat [th] thick
[ow] boat [hy] high [dh] that
[uh] book [jh] jet [dx] butter
[ey] bait [k] kick [v] vet
[er] bert [l] let [w] wet
[ay] buy [m] met [wh] which
[oy] boy [em] bottom
[arr] dinner [n] net [y] yet
[aw] down [en] button [z] zoo
[ax] about [ng] sing [zh] measure
[ix] roses [eng] washing
[aa] cot [-] silence

## Slide 38: The International Phonetic Alphabet
A standard that attempts to create a notation for all possible human sounds

## Slide 39: IPA Vowels
Caution: American English tongue positions don’t exactly match the chart. For example, ‘father’ in English does not have the tongue position as far back as the IPA vowel chart shows.

## Slide 40: IPA Diacritics

## Slide 41: IPA: Tones and Word Accents

## Slide 42: IPA: Supra-segmental Symbols

## Slide 43
Phoneme Tree Categorization
from Rabiner and Juang

## Slide 44
Characteristics: Vowels & Diphthongs
Vowels
  /aa/, /uw/, /eh/, etc.
  Voiced speech
  Average duration: 70 msec
  Spectral slope: higher frequencies have lower energy (usually)
  Resonant frequencies (formants) at well-defined locations
  Formant frequencies determine the type of vowel
Diphthongs
  /ay/, /oy/, etc.
  Combination of two vowels
  Average duration: about 140 msec
  Slow change in resonant frequencies from beginning to end

## Slide 45: Perception
Some perceptual components are understood, but knowledge concerning the entire human perception model is rudimentary
Understood Components
  The inner ear works as a bank of filters
  Sounds are perceived logarithmically, not linearly
  Some sounds will mask others

## Slide 46: The Inner Ear
Two sensory organs are located in the inner ear.
  The vestibule is the organ of equilibrium
  The cochlea is the organ of hearing

## Slide 47: Hearing Sensitivity Frequencies
Cochlea transforms pressure variations to neural impulses
Approximately 30,000 hair cells along basilar membrane
Each hair cell has hairs that bend to basilar vibrations
High-frequency detection is near the oval window.
Low-frequency detection is at far end of the basilar membrane.
Auditory nerve fibers are ``tuned'' to center frequencies.
Human hearing is sensitive to about 25 ranges of frequencies

## Slide 48: Basilar Membrane
Thin elastic fibers stretched across the cochlea
  Short, narrow, stiff, and closely packed near the oval window
  Long, wider, flexible, and sparse near the end of the cochlea
  The membrane connects to a ligament at its end.
Separates two liquid filled tubes that run along the cochlea
  The fluids are very different chemically and carry the pressure waves
  A leakage between the two tubes causes a hearing breakdown
Provides a base for sensory hair cells
  The hair cells above the resonating region fire more profusely
  The fibers vibrate like the strings of a musical instrument.
Note: Basilar Membrane shown unrolled

## Slide 49: Place Theory
Georg von Bekesy’s Nobel Prize discovery
  High frequencies excite the narrow, stiff part at the end
  Low frequencies excite the wide, flexible part by the apex
Auditory nerve input
  Hair cells on the basilar membrane fire near the vibrations
  The auditory nerve receives frequency coded neural signals
  A large frequency range possible; basilar membrane’s stiffness is exponential
Demo at: http://www.blackwellpublishing.com/matthews/ear.html
Decomposing the sound spectrum

## Slide 50: Hair Cells
The hair cells are in rows along the basilar membrane.
Individual hair cells have multiple strands or stereocilia.
  The sensitive hair cells have many tiny stereocilia which form a conical bundle in the resting state
  Pressure variations cause the stereocilia to dance wildly and send electrical impulses to the brain.

## Slide 51: Firing of Hair Cells
There is a voltage difference across the cell
  The stereocilia projects into the endolymph fluid (+60mV)
  The perylymph fluid surrounds the membrane of the haircells (-70mV)
When the hair cells moves
  The potential difference increases
  The cells fire

## Slide 52: Frequency Perception
We don't perceive speech linearly
Cochlea hair cell rows act as frequency filters
The frequency filters overlap
From early place theory experiments

## Slide 53: Sound Pressure Level (SPL)
Sound | dB
TOH | 0
Whisper | 10
Quiet Room | 20
Office | 50
Normal conversation | 60
Busy street | 70
Heavy truck traffic | 90
Power tools | 110
Pain threshold | 120
Sonic boom | 140
Permanent damage | 150
Jet engine | 160
Cannon muzzle | 220

## Slide 54: Absolute Hearing Threshold
The hearing threshold varies at different frequencies
Empirical formula to approximate the SPL threshold: SPL(f) = 3.65(f/1000)-0.8-6.5e-0.6(f/1000-3.3)^2+10-3(f/1000)4
Hearing threshold for men (M) and women (W) ages 20 through 60

## Slide 55: Sound Threshold Measurements
Note: The lines indicate the perceived DB relative to SPL for various frequencies
MAF = Minimum Audio Frequency

## Slide 56: Auditory Masking
Frequency Masking (sounds close in frequency)
  a sound masked by a nearby frequency.
  Lossy sound compression algorithms makes use of this
The temporal masking (sounds close in time)
  Strong sound masks a weaker sound with similar frequency
  Masking amount depends on the time difference
  Forward Masking (earlier sound masks a later sound)
  Backward Masking (later sound masks an earlier one)
Noise Masking (noise has random frequency range)
  Noise masks all frequencies.
  All speech frequencies must be increased to decipher
  Filtering of noise is required for speech recognition
A sound masks another sound that we can normally hear

## Slide 57: Time Domain Masking
Noise will mask a tone if:
  The noise is sufficiently loud
  The time difference is short
  Greater intensity increases masking time
There are two types of masking
  Forward: Noise masking a tone that follows
  Backward: A tone is masked by noise that follows
Delays
  beyond 100 − 200 ms no forward masking occurs
  Beyond 20 ms, no backward masking occurs. Training can reduce or eliminate the perceived backward masking

## Slide 58: Masking Patterns
A narrow band of noise at 410 Hz
From CMU Robust
Speech Group
Experiment
Fix one sound at a frequency and intensity
Vary a second sine wave’s intensity
Measure when the second sound is heard

## Slide 59: Psychoacoustics
Mel scale: Bark scale:
Formulas to convert linear frequencies to MEL and BARK frequencies
Apply an algorithm to mimic the overlapping cochlea rows of hair cells
Analyze audio according to human hearing sensitivity

## Slide 60: Mel Scale Algorithm
Apply the MEL formula to warp the frequencies from the linear to the MEL scale
Triangle peaks are evenly spaced through the MEL scale for however number of MEL filters desired
Start point of one triangle is the middle of the previous
End point to middle equals start point to middle
Sphinx speech recognizer: Height is 2/(size of un-scaled base)
Perform weighted sum to fill up filter bank array

## Slide 61: Frequency Perception Scale Comparison
Blue: Bark Scale
Red: Mel Scale
Green: ERB Scale
Equivalent Rectangular Bandwidth (ERB) is an unrealistic but
simple rectangular approximation to model the filters in the cochlea

## Slide 62: Formants
F0: Vocal cord vibration frequency (pitch)
  Averages: Male = 100 Hz, Female = 200 Hz, Children = 300 Hz
F1, F2, F3: Fundamental frequency harmonics
  Varies depending on vocal tract shape and length
  Articulators to the back brings formants together
  Articulators to the front moves formants apart
  Roundness impacts the relationship between F2 and F3
  Spreads out as the pitch increases
  Adds timbre (quality other than pitch or intensity) to voiced sounds
Advantage: Excellent feature for distinguishing vowels
Disadvantage: Not able to distinguishing unvoiced sounds

## Slide 63: Formant Example
“a” from “this is a demo”
Note: The vocal fold vibration is somewhat noisy, (a combination of frequencies)

## Slide 64: Formant Speaker Variance
Peterson and Barney recorded 76 speakers at the 1939 World’s Fair in New York City, and published their measurements of the vowel space in 1952.

## Slide 65: Vowel Characteristics
Demo of Vowel positions in the English language
http://faculty.washington.edu/dillon/PhonResources/vowels.html
Vowel | Word | high | Low | front | back | round | tense | F1 | F2
Iy | Feel | + | - | + | - | - | + | 300 | 2300
Ih | Fill | + | - | + | - | - | - | 360 | 2100
ae | Gas | - | + | + | - | - | + | 750 | 1750
aa | Father | - | + | - | - | - | + | 680 | 1100
ah | Cut | - | - | - | - | - | + | 720 | 1240
ao | Dpg | - | - | - | - | - | - | 600 | 900
ax | Comply | - | - | + | - | - | - | 720 | 1240
eh | Pet | - | - | - | + | + | + | 570 | 1970
ow | Tone | + | - | - | + | - | - | 600 | 900
uh | Good | + | - | - | + | - | + | 380 | 950
uw | Tool |  |  |  |  |  |  | 300 | 940
Demo: http://faculty.washington.edu/dillon/PhonResources/vowels.html

## Slide 66: Vowel Formants
ae
ah
aw
eh
ih
uh
e
o
u

## Slide 67
Frequency Domain: Vowels & Diphthongs
/ah/: low, back
/iy/: high, front
/ay/: diphthong

## Slide 68
Frequency Domain: Nasals
Nasals
  /m/, /n/, /ng/
  Voiced speech
  Spectral slope: higher frequencies have lower energy (usually)
  Spectral anti-resonances (zeros)
  Resonances and anti-resonances often close in frequency.

## Slide 69
Frequency Domain: Fricatives
Fricatives
  /s/, /z/, /f/, /v/, etc.
  Voiced and unvoiced speech (/z/ vs. /s/)
  Resonant frequencies not as well modeled as with vowels

## Slide 70
Frequency Domain: Plosives (Stops) & Affricates
Plosives
  /p/, /t/, /k/, /b/, /d/, /g/
  Sequence of events: silence, burst, frication, aspiration
  Average duration: about 40 msec (5 to 120 msec)
Affricates
  /ch/, /jh/
  Plosive followed immediately by fricative