## Slide 1: Speech Recognition Frameworks
Front End (Eliminate Redundancies)
  Digital Signal Processing
  Pre-process the audio signal to enhance speech and remove noise
  Extract relevant information for further processing
Back End (Recognition Algorithms)
  Phonetic labeling
  Pattern classification after training
  Statistical pattern-recognition
  Grammatical modeling for particular languages
  Dictionary data bases

## Slide 2: Definitions
Semi-stationary: Speech is a slowly changing (semi-stationary) signal considered to be static in a 20-50 MS time interval
Frame: A 20-50 MS portion of an audio signal
Feature: A calculated attribute of a speech frame
Window: An algorithm to smooth the edges of a frame
Noise: Artifacts in a signal that degrade its clarity

## Slide 3: Front End (Signal Processing)
Resample the simple to match the speech database sample rate
Filter noise
Enhance speech characteristics in the signal
Separate silence from speech; possibly detect phoneme boundaries
Partition into overlapping frames (about 25 MS with a 50% overlap)
For each frame
  Apply windowing algorithm to each frame to smooth edges
  Extract time domain features from the raw signal
  Extract frequency domain features after applying transformations to match human perception
  Possibly apply temporal smoothing algorithms
  Possibly transform the data to reduce the number of features
Feature normalization (mean to 0, variance to 1)

## Slide 4
Fourier
Transform
Cepstral
Analysis
Perceptual
Weighting
Time
Derivative
Time
Derivative
Energy
+
Mel-Spaced Cepstrum
Delta Energy
+
Delta Cepstrum
Delta-Delta Energy
+
Delta-Delta Cepstrum
Input Speech
Incorporate knowledge of the
nature of speech sounds in
measurement of the features.
Utilize rudimentary models of
human perception.
Acoustic Modeling: Feature Extraction Ecample
Measure features 100 times per sec.
Use a 25 MS window for frequency domain analysis.
Include absolute energy and 12 spectral measurements.
Time derivatives to model spectral change.

## Slide 5: Speech Frames
Breakup speech signal into overlapping frames
Why?
  Speech is quasi-periodic, not periodic, because vocal musculature is always changing
  Within a small window of time, we can assume constancy
Typical Characteristics
10-30 MS length
1/3 – 1/2 overlap
Goal: Extract short-term signal features from speech signal frames
Frame
Frame
Frame
Frame
Frame size
Frame
shift

## Slide 6: Feature Extraction
Definitions
  Feature: A calculated attribute of a speech signal
  Phoneme: The smallest phonetic unit that distinguishes words
  Morpheme: The smallest phonetic unit that conveys meaning
  Feature Extraction: Algorithm to convert a captured audio into a useable form for decoding
  Feature Vector: List of values representing a given signal frame
Process
  Signal Conditioning (digitizing a signal)
  Signal Measurement (compute signal amplitudes)
  Enhance (perform perceptual augmentations)
  Conversion (Convert data into a feature vector)
Challenge: Choose a relevant and computationally efficient feature set
Goal: Remove redundancies by representing a frame by its feature “fingerprint”

## Slide 7: Principle Component Analysis
Normalize the mean of the data set to zero
Calculate the covariance matrix and calculate the eigenvectors (v) and eigenvalues (λ) of that matrix
  Av = λv (ex:
Sort the eigenvectors (Vi) by eigenvalues
Pick the largest eigenvectors and discard those that remain.
Transform the data to a reduced dimension by performing a dot product (fNewp = )
Feature Dimension Reduction

## Slide 8: Which Audio Features?
Cepstrals: They are statistically independent and phase differences are removed
ΔCepstrals, or ΔΔCepstrals: Reflects how the signal is changing from one frame to the next
Energy: Distinguish the frames that are voiced verses those that are unvoiced
Normalized LPC Coefficients: Represents the shape of the vocal track normalized by vocal tract length for different speakers.
These are some of the popular speech recognition features

## Slide 9: Signal Processing Processing
Acoustic Transducers: Convert sound into an electronic signal which is then digitized
Sampling and Resampling: Down or up sample for compatibility with stored audio templates
Band pass filter: Eliminate frequencies that don’t contain useful speech information
Time Domain Analysis: Extract time domain features
Frequency Domain Analysis: Extract frequency domain features
Spectral Normalization: Apply Mel or Bark scale frequency transformations
Cepstral Analysis or Linear Prediction: Each have a well-defined set of steps
Feature Normalization: Normalize the mean, variance respectively to zero and one. Optionally nomalize the higher statistical moments.

## Slide 10: Speech Recognition Front End
Pre-emphasis
Time Domain
Features
Enhance and Consolidate Features
Spectral Analysis
windowing
Frequency
Features
Speech
Frame
Feature
Vector
(Frame by feature array)
Assume resampling is already done

## Slide 11: Pre-emphasis
Human Audio
  There is an attenuation of the audio signal loudness as it travels along the cochlea, which makes humans require less amplitudes in the higher frequencies
  Speech high frequencies have initial less energy than low frequencies
  De-emphasizing the lower frequencies compared to is closer to the way humans hear
Pre-emphasis Algorithm
  Pre-emphasis recursive filter de-emphasizes lower frequencies
  Formula: Y[i] = X[i] - (X[i-1] * δ)
  0.95 to 0.97 are common defaults for δ
  0.97 de-emphasizes lower frequencies more than 0.95

## Slide 12: Pre-emphasis Filter
y[i] = x[i] – x[i-1] * 0.95

## Slide 13: Windowing
Problem: Framing a signal results in abrupt edges
Impact
  There is significant spectral leakage in the frequency domain
  Large side lobe amplitudes
Effect of Windowing
  There are no abrupt edges
  Minimizes side lobe amplitudes and spectral leakage
How? Apply a window formula in the time domain (which is a simple for loop)
Definitions
Frame: A small portion (sub-array) of an audio signal
Window: A frame to which a window function is applied

## Slide 14: Window Types for Speech
Rectangular: wk = 1 where k = 0 … N
  The Naïve approach
  Advantage: Easy to calculate, array elements unchanged
  Disadvantage: Messes up the frequency domain
Hamming: wk = 0.54 – 0.46 cos(2kπ/N-1))
  Advantage: Fast roll-off in frequency domain, popular for ASR
  Disadvantage: worse attenuation in stop band
Blackman: wk = 0.42 – 0.5 cos(2kπ/(N-1)) + 0.08 cos(4kπ/(N-1))
  Advantage: better attenuation, popular for ASR
  Disadvantage: wider main lobe
Hanning: wk = 0.5 – 0.5 cos(2kπ/N-1))
  Advantage: Useful for pitch transformation algorithms
Multiply the window, point by point, to the audio frame

## Slide 15: Create and Apply Hamming Window
public double[] createHammingWindow(int filterSize)
{ double[] window = new double[filterSize];
double c = 2*Math.PI / (filterSize - 1);
for (int h=0; h<filterSize; h++)
window[h] = 0.54 - 0.46*Math.cos(c*h);
return window;
}
public double[] applyWindow(double[] window, double[] signal)
{ for(int i=0; i<window.length; i++) signal[i] = signal[i]*window[i];
return samples;
}

## Slide 16: Rectangular Window Frequency Response
Time Domain Filter

## Slide 17: Blackman & Hamming Frequency Response

## Slide 18: Time domain Features
Examples
Energy
Zero-crossing rate
Auto correlation and auto differences
Pitch period
Fractal Dimension
Linear Prediction coefficients
Advantages: less processing; usually easy to understand
Note: These features can directly be obtained from the raw signal

## Slide 19: Signal Energy
Calculate the short term frame energy
  Energy = ∑k=0,N (sk)2 where N is the size of the frame
Represent result in decibels relative to SPL db = 10 log(energy)
Tradeoffs
  If window is too small: too much variance
  If window is too big: encompasses both voiced and unvoiced speech
Useful to determine if a windowed frame contains a voiced speech
Voiced speech has higher energy than unvoiced speech or silence
Changes in energy can indicate stressed syllables (loudness contour)

## Slide 20: Zero Crossings
Eliminate a possible DC component, meaning every measurement is offset by some value
  Average the absolute amplitudes ( 1/M ∑ 0,M-1sk )
  Subtract the average from each value
Count the number of times that the sign changes
  ∑0,M-10.5|sign(sk)-sign(sk-1)|; where sign(x) = 1 if x≥0, -1 otherwise
  Note: |sign(sk)-sign(sk-1)| equals 2 if it is a zero crossing
Unvoiced speech tends to have higher zero crossing than background noise

## Slide 21: Pitch detection
Question: How well does a signal correlate with an offset version of itself?
Apply the auto-correlation formula
R = ∑i=1,n-z xf[i]xf[i+offset]/∑i=1,F xf[i]2
Apply the auto-difference formula
D = ∑i=1,n-z Math.abs(xf[i] - xf[i+offset])
Either method is useful for determining the pitch of a signal. We would expect that R is maximum (and D minimum) when offset corresponds to that of the pitch period
Determine self-similarity of a signal

## Slide 22: Vocal Source
Speaker alters vocal tension of the vocal folds
  If folds are opened, speech is unvoiced resembling background noise
  If folds are stretched close, speech is voiced
Air pressure builds and vocal folds blow open releasing pressure and elasticity causes the vocal folds to fall back
Average fundamental frequency (F0): 60 Hz to 300 Hz
Speakers control vocal tension alters F0 and the perceived pitch
Closed
Open
Pitch Period

## Slide 23: Fractal Dimension
Definition: The self-similarity of a signal
Comments
  There are various methods to compute a signal’s self-similarity, which each lead to different results
  Each method is empirical, not backed by mathematics
  Some popular algorithms
    Box Counting
    Katz
    Higuchi
  Importance: We would expect that the self-similarity of speech, because it is constrained by the larynx and vocal tract, to be different than that of background noise

## Slide 24: Box Counting Algorithm
delta = 1
FOR i = 0 to S
delta = 2^i
Cover the curve with rectangles: h = signal[i+delta] – signal[i], w = delta * t
Fractal[i] = count of rectangles needed to cover the curve
Perform a linear regression on the Fractal array
The slope of the best fit line is the fractal dimension
Assume signal[i] is an array of audio amplitudes, where each sample represents t milliseconds

## Slide 25: Linear Regression
Set of points: (x1,y1), (x2,y2), … (xN,yN)
Equations: Find b0 + b1x1 that minimizes errors where Yi = b0+b1xi+ei
Goal: Find slope b1 of the best fit line
Assumption: the expected value (mean) of the errors is zero
Note: X’ is transpose of X, -1 is inverse

## Slide 26: Best Fit Slope of x amplitudes
bestFit(double[] y)
{ int MAX = y.length;
// Compute the X’X matrix (aij)
double d = MAX*(MAX+1)*(2*MAX+1)/6; // ∑ xi2 = d
double b = MAX * (MAX + 1) / 2; // ∑ xi = b = c
double c = b, a = MAX; // number of points
double sumXY=0, sumY=0; // Compute ∑ yi and sum ∑ xi * yi bi = X’y
for (int i=0; i<MAX; i++) { sumXY += (i+1) * y[i]; sumY += y[i]; }
// Return (X’X)-1 * X’y, where (X’X)-1 is the inverse of X’X
double numerator = -c*sumY + a*sumXY ; // -c*sumXY+a*sumY
double denominator = d * a – b * c; // ad - bc
return (denominator == 0) ? 0 : numerator / denominator; // Slope
}
Assuming that the x points are 1, 2, 3, …
Note:
Method returns b1 of y = b0 + b1x

## Slide 27: Katz Fractal Dimension
double katz(double[] x)
{ int N = x.length;
if (N<=1) return 0;
double L=0, diff=0, D=0;
for (int i=1; i<x.length; i++)
{ L += Math.abs(x[i] - x[i-1]);
diff = Math.abs(x[0] – x[i]);
if (diff > D) D = diff;
}
double log = Math.log10(N-1);
return (d==0)?0:log/(Math.log10(d/L)+log);
}
L = ∑ xi – xi-1 (sums adjacent lengths)
max, min = from first point
Katz normalizes log(L)/log(D)) to use log(L/d)/log(D/d)
Final formula log(L/d)/log(D/d) =
log(N - 1) / log(D/(L/(N-1))) =
log(N-1) / (log(D/m) + log(N-1))
Notes
  N-1 because there are N-1 intervals with a signal of N points
  L / d = L / (L/(N-1)) = N-1
Dimension = log(sum of lengths)/log(largest distance from the first point)

## Slide 28: Higuchi Fractal Dimension

## Slide 29: Higuchi Fractal Dimension (cont)
public double higuchi (double[] x)
{ int MAX = x.length/4;
double[] L = new double[MAX];
for (int k=1; k<=MAX; k++)
{ L[k-1] = Lk(x, k)/k; }
// Find least squares linear best fit of L
double slope = bestFit(L, MAX) + 1e-6;
return Math.log10(Math.abs(slope));
}
double Lk(double[] x, int k)
{ double sum = 0;
for (int m=1; m<=k; m++)
{ sum += LmK(x, m, k); }
return sum / k;
}
double LmK(double[] x, int m, int k)
{ int N = x.length;
double sum = 0;
for (int i=1; i<=(N-m)/k; i++)
{ sum += Math.abs
(x[m-1+i*k]-x[m-1+(i-1)*k]);
}
return sum * (N - 1) / ((N - m)/k * k);
}

## Slide 30: Linear Prediction Coding (LPC)
Originally developed to compress (code) speech
Although coding pertains to compression, LPC has much broader implications
  LPC is equivalent to the tubal model of the vocal tract model
  LPC can be used as a filter to reduce noise (Wiener filter) from a signal
  A speech frame can be approximated with a set of LPC coefficients
    one coefficient per 1k of sample rate + 2
    Example: For a 10k sample, 12 LPC coefficients are sufficient
  LPC speech recognition is somewhat noise resilient

## Slide 31: Illustration: Linear Prediction
{1, 2, 3, 4, 5, 6, 7, 8, 9, 10, 11, 12, 13, 14, 15, 16}
Goal: Estimate yn using the three previous values
yn ≈ a1 yn-1 + a2 yn-2 + a3 yn-3
Three ak coefficients, Frame size of 16, 3 coefficients
Thirteen equations and three unknowns
Note: No solutions, but LPC finds coeffients with the smallest error

## Slide 32: Solving n equations and n unknowns
Gaussian Elimination
  Complexity: O(n3)
Successive Iteration
  Complexity varies
Cholesky Decomposition
  More efficient, still O(n3)
Levenson-Durbin
  Complexity: O(n2)
  Works for symmetric Toplitz matrices
Definitions for any matrix, A
Transpose (AT): Replace aij by aji for all i and j
Symmetric: AT = A
Toplitz: Diagonals to the right all have equal values

## Slide 33: Covariance Example
Signal: {…, 3, 2, -1, -3, -5, -2, 0, 1, 2, 4, 3, 1, 0, -1, -2, -4, -1, 0, 3, 1, 0, …}
Frame: {-5, -2, 0, 1, 2, 4, 3, 1}, Number of coefficients: 3
φ(1,1) = -3*-3 +-5*-5 + -2*-2 + 0*0 + 1*1 + 2*2 + 4*4 + 3*3 = 68
φ(2,1) = -1*-3 +-3*-5 + -5*-2 + -2*0 + 0*1 + 1*2 + 2*4 + 4*3 = 50
φ(3,1) = 2*-3 +-1*-5 + -3*-2 + -5*0 + -2*1 + 0*2 + 1*4 + 2*3 = 13
φ(1,2) = -3*-1 +-5*-3 + -2*-5 + 0*-2 + 1*0 + 2*1 + 4*2 + 3*4 = 50
φ(2,2) = -1*-1 +-3*-3 + -5*-5 + -2*-2 + 0*0 + 1*1 + 2*2 + 4*4 = 60
φ(3,2) = 2*-1 +-1*-3 + -3*-5 + -5*-2 + -2*0 + 0*1 + 1*2 + 2*4 = 36
φ(1,3) = -3*2 +-5*-1 + -2*-3 + 0*-5 + 1*-2 + 2*0 + 4*1 + 3*2 = 13
φ(2,3) = -1*2 +-3*-1 + -5*-3 + -2*-5 + 0*-2 + 1*0 + 2*1 + 4*2 = 36
φ(3,3) = 2*2 +-1*-1 + -3*-3 + -5*-5 + -2*-2 + 0*0 + 1*1 + 2*2 = 48
φ(1,0) = -3*-5 +-5*-2 + -2*0 + 0*1 + 1*2 + 2*4 + 4*3 + 3*1 = 50
φ(2,0) = -1*-5 +-3*-2 + -5*0 + -2*1 + 0*2 + 1*4 + 2*3 + 4*1 = 23
φ(3,0) = 2*-5 +-1*-2 + -3*0 + -5*1 + -2*2 + 0*4 + 1*3 + 2*1 = -12
Note: φ(j,k) = ∑n=start,start+N-1 yn-kyn-j

## Slide 34: Auto Correlation Example
Signal: {…, 3, 2, -1, -3, -5, -2, 0, 1, 2, 4, 3, 1, 0, -1, -2, -4, -1, 0, 3, 1, 0, …}
Frame: {-5, -2, 0, 1, 2, 4, 3, 1}, Number of coefficients: 3
R(0) = -5*-5 + -2*-2 + 0*0 + 1*1 + 2*2 + 4*4 + 3*3 + 1*1 = 60
R(1) = -5*-2 + -2*0 + 0*1 + 1*2 + 2*4 + 4*3 + 3*1 = 35
R(2) = -5*0 + -2*1 + 0*2 + 1*4 + 2*3 + 4*1 = 12
R(3) = -5*1 + -2*2 + 0*4 + 1*3 + 2*1 = -4
Note: φ(j,k)=∑n=0,N-1-(j-k) ynyn+(j-k)=R(j-k)
Assumption: all entries before and after the frame treated as zero

## Slide 35: LPC Features as a front end
Assumptions
  Future discrete signal samples are functions of the previous ones
  The speech signal is purely linear (interactions with other signials add or subtract, but don’t multiply)
Coefficients: Generally eight to fourteen LPC coefficients are sufficient to represent a particular block of sound samples
Disadvantage: Linear prediction coefficients tend to be less stable other methods (ex: Cepstral analysis).
Enhancement: Perceptual Linear Prediction uses both frequency and time domain data. The result is comparable to Cepstral analysis. Rasta Linear Prediction also filters adjacent samples for an additional enhancement.

## Slide 36: The LPC Spectrum
Perform a LPC analysis
Find the poles
Plot the spectrum around the z-Plane unit circle
What do we find concerning the LPC spectrum?
Adding poles better matches speech up to about 18 for a 16k sampling rate
The peaks tend to be overly sharp (“spiky”) because small radius changes greatly alters pole skirt widths in the z-plane

## Slide 37: Filter Bank Front End
The bank consists of twenty to thirty overlapping band pass filters spread along the warped frequency axis
Represent spectrum with log-energy output from filter bank
Each frequency bank F handles frequencies from f-i to f+i or individual ranges of frequencies that models the rows of hair bands in the cochlea
The feature data is an array of energy values obtained from each filter
Result: Good idea, but it has not proven to be as effective as other methods

## Slide 38: Warped band pass filter set
Mel frequency warping
Original Spectrum

## Slide 39: Signal Filters
Purposes (General)
Examples
Separate Signals
Eliminate distortions
Remove unwanted data
Compress and decompress
Extract important features
Enhance desired components
Eliminate frequencies without speech information
Enhance poor quality recordings
Reduce background Noise
Adjust frequencies to mimic human perception
How? Execute a convolution algorithm

## Slide 40: Convolution
public static double[] convolution(double[] x, double[] b, double[] a)
{ double[] y = new double[x.length + b.length - 1];
for (int i = 0; i < x.length; i ++)
{ for (int j = 0; j < b.length; j++)
{ if (i-j>=0) y[i] += b[j] * x[i - j]; }
if (a!=null)
{ for (int j = 1; j < a.length; j ++)
{ if (i-j>=0) y[i] -= a[j] * y[i - j]; }
}
}
return y;
}
The algorithm for creating Time Domain filters
Notes:
The symbol x commonly represents the raw time domain signal
The symbol Y represents the filterd signal
Capital X represents the frequency domain spectrum

## Slide 41: Time Domain Filters
Finite Impulse Response
  Filter only affects the data samples, hence the filter only effects a fixed number of data point
  y[n] = b0 sn+ b1 sn-1+ …+ bM-1 sn-M+1=∑k=0,M-1bk sn-k
Infinite Impulse Response (also called recursive)
  Filter affects the data samples and previous filtered output, hence the effect can be infinite
  t[n] = ∑k=0,M-1bk sn-k + ∑k=0,M-1 ak tn-k
If a signal was linear, so is the filtered signal
  Why? We summed samples multiplied by constants, we didn’t multiply or raise samples to a power

## Slide 42: Convolution Theorem
Multiplication in the time domain is equivalent to convolution in the frequency domain
Multiplication in the frequency domain equivalent to convolution in the time domain
Application: We can design a filter by creating its desired frequency response and then perform an inverse FFT to derive the filter kernel
Theoretically, we can create an ideal (“perfect”) low pass filter with this approach

## Slide 43: Amplify
Top Figure (original signal)
Bottom Figure
  The signal’s amplitude is multiplied by 1.6
  Attenuation can occur by picking a magnitude that is less than one
y[n] = k δ[n]

## Slide 44: Moving Average FIR Filter
int[] average(int x[])
{ int[] y[x.length];
for (int i=50; i<x.length-50; i++)
{ for (int j=-50; j<=50; j++) { y[i] += x[i + j]; }
y[i] /= 101;
} }
Convolution using a simple filter kernel
Formula:
Example Point:
Example Point (Centered):

## Slide 45: IIR (Recursive) Moving Average
Example: y[50] = (x[47]+x[48]+x[49]+x[50]+x[51]+x[52]+x[53])/7 y[51] = (x[48]+x[49]+x[50]+x[51]+x[52]+x[53]+x[54])/7 = y[50] + (x[54] – x[47])/7
The general case y[i] = y[i-1] + (x[i+M/2] - x[i-(M+1)/2])/M
Two additions per point no matter the length of the filter
Note: Integers work best with this approach to avoid round off drift

## Slide 46: Moving Average Filter Characteristics
Longer kernel filters more noise
Long filters lose edge sharpness
Distorts the frequency domain
Very fast
Frequency response
  sync function (sin(x)/x)
  A degrading sine wave
Speech
  Great for smoothing a pitch contour
  Horrible for identifying formants

## Slide 47: Time Domain Filtering
Band Pass
  Filter frequencies below the minimum fundamental frequency (F0)
  Filter frequencies above the speech range (≈4kHz)
Linear smoother and median of five filters
  Used in combination to smooth the pitch contour
Derivative (slope) filter
  Measure changes in a given feature from one frame to another
  Tends to reduce the effects of noise in ASR
Noise Removal: Separate set of slides

## Slide 48: Band Pass Filters
Butterworth
  Advantages:
    IIR filter, which is fast
    minimal ripple
  Disadvantage: slow transition
Window Sync
  Advantage: quick transition
  Disadvantages
    FIR filter, which is slow
    Ripples in the pass band
Many other filters with various advantages and disadvantages. Open source code for these exist.
ACORNS uses both Butterworth and Window Sync filters

## Slide 49: Median of Five
private void medianOfFive(int feature)
{ double median, save, middle, out[] = new double[features.length];
for (int frame=2; frame<features.length - 2; frame++)
{ median = features[frame+2][feature];
save = features[frame+1][feature];
if (median > save) { median = features[frame+1][feature];
save = features[frame+2][feature]; }
if (features[frame-2][feature]<features[frame-1][feature])
{ if (features[frame-2][feature]>median) median= features[frame-2][feature];
if (features[frame-1][feature]<save) save = features[frame-1][feature];
} else
{ if (features[frame-1][feature]>median) median= features[frame-1][feature];
If (features[frame-2][feature]<save) save = features[frame-2][feature];
}
middle = features[frame][feature];
if ((save - middle) * (save-median) <= 0) median = save;
if ((middle - save) * (middle - median) <= 0) median = middle;
out[frame] = median;
}

## Slide 50: Linear Smoother
private double[] linearSmoother (int frame, double[][] frames, int feature)
{ double[] out = new double[features.length];
for (int feature = 2; frame<frames[frame].length; frame++)
{
out[feature] = frames[frame][feature]/4
+ frames[frame-1][feature]/2
+ frames[frame-2][feature]/4;
} return out;
}

## Slide 51: Derivative Filter
private void calculateDynamicFeatures(int featureOffset)
{ int start, end;
double numerator, denominator;
for (int frame=0; frame<features.length; frame++)
{ numerator = denominator = 0;
start = (frame<D) ? -frame: - D;
end = (frame>=features.length - D) ? features.length - frame - 1: +D;
for (int d= start; d<= end; d++)
{ numerator += d * features[frame + d][feature];
denominator += d * d;
}
if (denominator !=0) out[frame][feature] = numerator / denominator;
} }
Computes slope over 2D+1 frames

## Slide 52: Filter Characteristics
Note: The ideal filter would require infinite computation

## Slide 53: Filter Terminology
Rise time: Time for step response to go from 10% to 90%
Linear phase: Rising edges match falling edges
Overshoot: amount amplitude exceeds the desired value
Ripple: pass band oscillations
Ringing: stop band oscillations
Pass band: the allowed frequencies
Stop band: the blocked frequencies
Transition band: frequencies between pass or stop bands
Cutoff frequency: point between pass and transition bands
Roll off: transition sharpness between pass and stop bands
Stop band attenuation: reduced amplitude in the stop band

## Slide 54: Filter Performance